## Slide 1: Joint Architecture for Unmanned Systems
January 29, 2011
Presented by Daniel Barber
University of Central Florida
Institute for Simulation and Training
ACTIVE Laboratory
Based on Slides by Bo Sun

## Slide 2: JAUS
Standard for Unmanned Systems originally initiated by the U.S. DoD
Open and scalable service-based architecture
Designed to be:
  Vehicle platform independent
  Mission isolated
  Hardware and technology independent

## Slide 3: JAUS
Defines “Services” and the interfaces to them
In essence, a description of a vocabulary to access capabilities
  Between and within Unmanned Systems
  Between Unmanned Systems and the Operator Control Unit (OCU)
  Described by the JAUS Service Interface Definition Language (JSIDL)

## Slide 4: Why JAUS?
To provide
  A basis for logical interoperability
  A foundation for achieving automated architectures

## Slide 5: Significance of JAUS
Allows
  Interoperability
  Reduction in cost of support
  Reduction in cost of development
  Ease of unmanned system modeling

## Slide 6: History of JAUS
Spearheaded by the DoD under the Joint Robotics Program
JAUS Reference Architecture published by JAUS Working Group
SAE JAUS Standard Documents maintained by the AS4 Unmanned Systems Technical Committee
Notes: Jaus RA and SAE JAUS are vastly different.

## Slide 7: Jaus ra VS. sae-jaus
JAUS Reference Architecture (RA) was the original version of the standard, which is no longer maintained after version 3.3, and is a component based message passing architecture
SAE-JAUS is the current version of the standard and contains more formal documentation and clearer guidelines to support implementation. It is a service-based architecture. The current standards documents are:
  AS5669 - JAUS Transport Standard – Defines packet construction and addressing for TCP, UDP, and Serial links
  AS5710 – JAUS Core Service Set – Establishes common set of services for distributed systems communication and coordinate
  AS6009 – JAUS Mobility Service Set – Migrates mobility related components from JAUS RA to SAE standard (e.g. Primitive Driver, Waypoint Drivers)

## Slide 8: Open source JAUS Implementations
Name | JAUS Version
JAUS Tool Set | SAE JAUS
OpenJAUS | JAUS RA 3.3
Junior Middleware | SAE JAUS - AS5669A Only
JAUS++ | JAUS RA 3.3 (v1.X) SAE-JAUS (v2.X)
RI-JAUS | JAUS RA 3.3

## Slide 9: JAUS Topology
System
UGV
Sensor PC
Navigation PC
OCU
Control PC
System
Subsystem
Node
Component
Omni Sensor
AV Sensor
AV Display
Navigator
Notes: System –Collection of subsystems
Subsystem – A complete vehicle (e.g. UGV)
Node – Any device with a physical address (e.g. PC with IP address or serial link)
Component – Software application running on a node, and is composed of services

## Slide 10: Component AND Services
A Component is a part of or a complete software application running on a Node and is composed of Services
A Service is a defined capability with a formal interface to access or manipulate that capability
For example, consider a car radio as a Component with two Services (clock and music). The clock as buttons and display to change the time and show you the current reading. The music service has a knob and speaker which manipulate the volume of the sound and allow you to hear it
Services can inherit from other services in order to extend capabilities defined

## Slide 11: JAUS components and services
Component
Transport Service
Service X
Service Y
Service Z
Component
Transport Service
Service X
Service Y
Component
Transport Service
Service X
Service Y
Service Z
Node
Node
Subsystem
Subsystem
Physical Transport Layer (e.g. JUDP)

## Slide 12: JAUS SERVICE Messages
Three types of messages to interface with a Service
  Query
  Report
  Command (need control)

## Slide 13: Core Service set AND TOPOLOGY
Transport
Events
Access Control
Management
Time
Liveness
Discovery

## Slide 14: Transport Service
Defines
  TCP (JTCP), UDP (JUDP), and Serial (JSerial) links
  General packet header and payload format
    Message type
    Source/destination addressing
Software Defined Protocol

## Slide 15: Events Service
Create Event (periodic or on change)
Confirm Event Request
Cancel Event
Query Events
Report Events
Dogbot, tell me when you move!
OK!

## Slide 16: Access Control Service
Request Control
Confirm Control
Query Authority
Report Authority
Dogbot, grant me control of your services!
OK!

## Slide 17: Liveliness Service
Query Heartbeat Pulse
Report Heartbeat Pulse
Dogbot, are you there?
Still kicking!

## Slide 18: Time Service
Query Time
Report Time
Set Time
Dogbot, What time is it?
4:19pm

## Slide 19: Discovery Service
Provides topology of Subsystem Configuration
Provides list of services available per component
I wonder who is there!?
Dogbot is here!
Tell me what you can do?
I can tell time and be driven

## Slide 20: Management Service
Provides component States: Ready, Standby, Emergency
Shutdown, Reset controlled components
Dogbot, Shutdown!
zzzzzzzzzz…

## Slide 21: MOBILITY Service set AND TOPOLOGY
Access Control
Global Pose Sensor
Local Pose Sensor
Velocity State Sensor
Management
Primitive Driver
Global Waypoint Driver
Local Waypoint Driver

## Slide 22: Primitive driver Service
Provides mechanism to directly manipulate actuators/motors on a platform
Uses “Wrench Efforts” which are percent of effort along or around the vehicles coordinate frame
Dogbot, move at 50% effort on the X Axis
Driving Forward at 50% Max Effort

## Slide 23: Global Pose Service
Provides position and attitude information: Latitude, Longitude, Roll, Pitch, Yaw, etc.
Dogbot, tell me when your Global Pose Changes
Confirm Event Request
Report Event – Global Pose

## Slide 24: Questions?